## Slide 1
Modular Distributed
Ammonia Synthesis
AIChE Student Contest Problem
ChemE 486
Process Design II
March 30, 2020

## Slide 2
OFFICIAL PROBLEM STATEMENT & RULES
“AIChE 2019 – 2020 Student Design Competition Problem Statement & Contest Rules”
These notes are condensed version of the AIChE document
The AIChE document is the official statement of the problem and rules
These notes do not alter the AIChE problem statement and rules
When in doubt, consult the AIChE document, the instructors, or http://studdentchapters@aiche.org

## Slide 3
TECHNICAL ADVISING RULE
“Chemical Engineering Departments, including advisors, faculty, or any other instructors, cannot provide technical aid specifically directed at the solution of the AIChE Student Design Competition if students plan on submitting to the contest. Please inform your Chemical Engineering Department about the rules for this competition so that they do not provide technical aid that would be a violation of the competition rules.”
For fairness, this rule applies in this class to all groups, even if they do not plan to submit their design

## Slide 4
SUBMISSION OF DESIGN
Two categories of solutions
  Individual
  Team (group of ≤ 4 members)
Up to two submissions for each solution category
All students, working individually or in a group, must be members of AIChE to submit
Instructors select among the solutions and submit on behalf of the students

## Slide 5
MORE RULES
Problem statement for our class issued March 30, 2020 (today)
60 days allowed for solution
Due date for our class is Friday May 29, 2020
All pertinent data are contained in the problem statement and accompanying references
Other sources (library, internet, journals, etc.) may be consulted, but data used for calculations and evaluation are to come only from the problem statement

## Slide 6
STUDENT GUIDANCE
Students may ask general questions of instructors and TAs
  See example on two types of H2 production in AIChE problem statement
  Questions on simulation software allowed
Students must not share or seek information from
  486 students outside their group
  Other students/TAs/faculty at UW
  Students/TAs/faculty at other universities
  Anyone!

## Slide 7
AIChE’s EVALUATION OF SOLUTIONS
Substantial correctness of results and soundness of conclusions
Ingenuity and logic employed
Accuracy of calculations
  interpreted as freedom from mistakes
  Extreme precision is not necessary
Form of presentation
Two awards in each category (individual & team)
  Best overall solution
  Best implementation of process safety principles

## Slide 8
SOLUTION FORMAT
Exact requirements in AIChE problem statement
No references to
  Names of students, TAs, instructors
  The University of Washington (either in words, logos, or mascots)
  (Report is to be anonymous)
Electronic submission in PDF or Word formats
125 pages or less
Up to 100 additional pages allowed for supplemental material

## Slide 9
PROBLEM STATEMENT
Modular distributed ammonia synthesis
Alternatives to ammonia production supply chain
Located near point-of-use in US Corn Belt
50 metric tonnes per day (50 mtpd) continuous production rate
Production rate accounts for seasonal and other variations
Anhydrous ammonia ≥ 99.5% by mass

## Slide 10
MODULAR MANUFACTURING METHODS
Pre-fabricated processes or sub-sections of processes
50 mtpd production rate << typical 1,000 mtpd production rate
Need to consider loss of economy of scale

## Slide 11
POINTS TO CONSIDER
May combine smaller (< 50 mtpd) or unit-scale modules in parallel to achieve desired production rate
Invoke process intensification (PI) when possible
  PI: Accomplish multiple objectives in process unit
Minimize carbon footprint
Develop innovative design so as to minimize intellectual property (IP) licensing

## Slide 12
ADDITIONAL POINTS
Consider the following in designs and recommendations
  Safety
  Financial/technical risk
  Environmental aspects
Economic parameters
  Useful plant life: 20 years
  Minimum acceptable rate of return (discount rate): 8%

## Slide 13
UPSTREAM PROCESS ALTERNATIVES
N2: separation from air (various methods)
H2: steam methane reforming (SMR) with water gas shift (WGS)
H2: Electrolysis of water (with renewable electricity)

## Slide 14
DOWNSTREAM PROCESS ALTERNATIVES
Ammonia synthesis loop (Haber-Bosch)
  Traditional process
  Iron catalyzed
  Conversion 20% per pass (typical)
  High recycle rate
  High temperature and 60 – 180 bar

## Slide 15
DOWNSTREAM PROCESS ALTERNATIVES (cont.)
Ammonia absorption with reactive separation
  Developed at University of Minnesota
  MgCl2 absorbent
  Conversions over 90%
  Complex system with high capital cost
Non-thermal plasma catalysis (NTP)
  Use renewable electricity
  High conversion
  Atmospheric pressure
Streamline WGS and gas purification
These alternatives all involve PI

## Slide 16
CHOICE OF PROCESS ALTERNATIVES
Suggested alternatives are starting points
May choose from among any of the alternatives
Explain rationale for choice of process
May use other alternatives not listed in problem statement

## Slide 17
MODULAR PLANT ECONOMIC CONSIDERATIONS
Heuristic methods
  Good for early design stages
  Power-law scaling
  Uncertainty in extrapolation to small scale
Vendor quotes
Lang factors, Guthrie factors, and others
  Not intended for small scale
  When in doubt, be conservative
Other methods

## Slide 18
MODULAR MANUFACTURING
Unitary
  Modules of process units (air sep. reactor, etc.)
  Modules pre-fabricated
  Assembled on-site
  “Cubing” the project
Parallel
  Choose unit scale of process (e.g. 10 mtpd)
  Pre-fabricate module at unit scale
  Add modules in parallel to achieve desired production rate
  Economy of mass production (Experience Curve)

## Slide 19
PLANT LOCATION
Minnesota River Valley
High ammonia demand (corn needs lots of fertilizer)
High wind power
See maps in problem statement

## Slide 20
ENVIRONMENT CONSIDERATIONS
Minimize environmental impacts
Use best available control technology (BACT) for waste treatment
Accommodate permitting process
  > 6 months for each permit submission
  30 – 34 months for modular plant
Design must include all gaseous, liquid, and solid waste streams along with BACT for treatment prior to discharge

## Slide 21
HEALTH CONSIDERATIONS
Scan for health risks (SDS)
Must include table of all key health risks and steps to mitigate

## Slide 22
SAFETY CONSIDERATIONS
Definition by Center for Chemical Process Safety (CCPS)
  Chemical process safety is a …
  “disciplined framework for managing the integrity of operating systems and processes handling hazardous substances by applying good design principles, engineering and operating practices.”
CCPS “20 Elements of Risk-Based Process Safety”
CCPS Process Safety Pillar: “Learn from Experience”
EHS Resources for ammonia manufacturing
Design should include relevant lessons learned from industry and how they were incorporated in the design

## Slide 23
Have a great quarter,
and
stay healthy!